## Slide 1: Aerosols and Climate, Past and Present Results from the Physics Department NOAA/NSF Greenland site
Thomas A Cahill and the
UC Davis DELTA* Group (1994- present)
Dr. David Barnes (until 2015), typically 1 or 2 grad students, 2 Physics and 2 Engineering UG students, and 1 or 2 non-UCD faculty collaborators
Detection and Evaluation of Long-range Transport of Aerosols,
with major support from the College of Engineering

## Slide 2: Take home message: The Earth balances on an energy knife edge, and 12,000 years ago, it fell off. (… and it seriously wobbled in 1816…)
Past disasters with aerosol components:
    The “Snowball/Slushball Earths”,
    Permian and Yucatan extinctions
Aerosols and climate, - 450 kyears to – 1,000 years
    The Ice ages and the Younger Dryas mystery
    UCD data on Greenland ice cores
Aerosols and climate, - 1,000 years to + 85 years
    Current climate change
    UCD data on Greenland aerosols

## Slide 3: Short wavelength cycle,
Sunlight (6000 K, 0.4 to 0.6 m), 1353 w/m2
100%
31%
4%
2/3 oceans, 1/3 land
rain
19%
50%
Variable, average = 46%
23%
10%
(albedo = 0.09)
= 100%

## Slide 4: Back scattering of incoming solar radiation
Kλ = /r2 approaches 2
Kλ = /r2 approaches 5
Blue sky ~ 1/4
Reflected light
Light from the sun
Too few aerosol particles to scatter light effectively:
Clouds

## Slide 5: MODIS, 08/08/2008; T avg =29.7 C, RH avg = 72%, rain = 0.0 cm, Vw = 8.3 km/hr, Visibility = 3.6 km, PM10 = 156 g/m3
Beijing

## Slide 6: Scattering efficiency Kλ = /r2 per particle Size parameter  = 2r Nm/λ (~ π D/λ)
mi = 0, pure scattering; mi = 1, pure absorption
Diameter  
Pure scattering – water, sulfates, nitrates,..
Pure absorbing - soot, …
Optically efficient aerosols
Too few aerosol particles to scatter light effectively: exception - clouds

## Slide 7: Standard assumption of the size distribution of ambient air aerosols < 1970

## Slide 8: Typical size distribution of ambient air aerosols > 1970 with optically efficient aerosols shaded
Accumulation mode - long atmospheric lifetimes – nitrates, sulfates, wood smoke…
Mechanical mode – short atmospheric lifetimes- dust, sea salt, pollen, …
Diffusion and condensation
Gravitation vs air viscosity
Optically efficient aerosols

## Slide 9: Measuring aerosols? Some options used in the 1970’s by the most successful groups
US EPA/CA ARB 24 hr mass
U. Minnesota several hr mass vs size
U Nevada, DRI many hr chemistry vs size
Lund, Sweden several hr elements vs size (PIXE)
Florida State continuous elements vs time
UC Riverside continuous size and time (drum)
    I used UC Riverside’s rotating drum impactor and added the Swedish technique Proton Induced X-Ray Emission (PIXE) from our cyclotron, and then innovated from that base.
UC Davis continuous size, time, elements
  .

## Slide 10: Typical size distribution of ambient air aerosols > 1970 with optically efficient aerosols shaded
Accumulation mode - long atmospheric lifetimes – nitrates, sulfates, wood smoke…
Mechanical mode – short atmospheric lifetimes- dust, sea salt, pollen, …
Optically efficient aerosols
1 particle
1,000 particles
106 particles
Aerosols that dominate global albedo

## Slide 11: Long wavelength cycle
100%
31%
4%
60%
2/3 oceans, 1/3 land
Earth, (300 K, 10 m, 338 w/m2 )
rain
105%
119%
19%
Greenhouse effect ~ + 30 C
50%
Variable, average = 46%
23%
10%
113%
6%
= 100%
aerosols
gasses
31% = 3 % Rayleigh + 12% Mie (very fine) + ~ 1% Mie (coarse) + 15% clouds
Sunlight (6000 K, 0.4 to 0.6 m), 1353 w/m2

## Slide 12: The Earth’s energy balance is critically dependent on the global albedo.
Albedo of ocean water ~ 0.06, or ~ 6% of all light reaching the surface is reflected
Forests and meadows, ~10%
Sand and deserts ~ 28%
Volcanic eruptions, dust storms ~ 40% ± 15%
Clouds ~ 50%
Albedo of ice and snow is ~ 60%

## Slide 13: Map of the Earth, ~ 850 to 650 million years ago

## Slide 14: One model of a Slushball Earth: Requirements: 1. Significant continental land mass near the equator, and 2. A trigger event cools a) asteroid impact b) super volcano c)other 3. Snow at low latitudes – albedo from 0.28 to 0.60; then oceans start to freeze, from 0.06 to 0.60 4. Locks into a Slushball phase
Flood basalt events

## Slide 15: One model of a Slushball Earth: Requirements: 1. Significant continental land mass near the equator, and 2. A trigger event a) asteroid impact b) super volcano c)other 3. What brought us out of it? a) CO2 rose to 13% (vs current 0.04%) b) oceans thaw c) eventually the land mass split up
Flood basalt events

## Slide 17
Axial precession 26,000 years
Eccentricity 96,000 and 413,000 years
Benthic forams 18O (‰)
Vostok ice core
Milankovitch Cycles
kiloyears
Eccentricity 96,000 and 413,000 years
Axial precession 26,000 years
Temperature from benthic forams (shells) 18 O
Good news? If you solve this problem, you will be famous!
Bad news: We are seriously messing with a climate system we don’t fully understand
Temperature from ice cores

## Slide 18
?
Greenland cores

## Slide 19: Did a volcano trigger a sudden cooling of the Earth?
Iceland, April 17, 2010, Eyjafyallajokull, Volcanic Explosive Index (VEI) 4
5 | > 25 km | 1 to 10 km3 | Plinian | St. Helens (1980)
6 | > 25 km | 10 to 100 km3 | Plinian – Ultra Plinian | Krakatau (1883) ( ~ 1.2 C)
7 | > 25 km | 100 to 1000 km3 | Ultra Plinian | Pinatubo (1991) (-0.5 C) Tambora (1815) 150 km 3
8 | > 25 km | 1,000 km3 2,800 km3 2,400 km3 5,000 km3 | Ultra Plinian | Taupo (25 ka) Toba (74 ka), Yellowstone, (2.1 ma) La Garita, CO (25 ma)

## Slide 20: New chemical data from shallow cores in Antarctica
Tambora eruption, 1815. 1816 was
“the year without a summer”
Pinatubo 1991 global temp – 0.5 C
Krakatoa 1883
global temp -1.2 C
The warm cycle to Ice Age temperature swing is about - 10 to - 12 C
Temperature estimate, - 3 to - 4 C

## Slide 21: Did a volcano trigger a sudden cooling of the Earth?
Iceland, April 17, 2010, Eyjafyallajokull, Volcanic Explosive Index (VEI) 4
5 | > 25 km | 1 to 10 km3 | Plinian | St. Helens (1980)
6 | > 25 km | 10 to 100 km3 | Plinian – Ultra Plinian | Krakatau (1883) ( ~ 1.2 C)
7 | > 25 km | 100 to 1000 km3 | Ultra Plinian | Pinatubo (1991) (-0.5 C) Tambora (1815)
8 | > 25 km | 1,000 km3 2,800 km3 2,400 km3 5,000 km3 | Ultra Plinian | Taupo (25 ka) Toba (74 ka), Yellowstone, (2.1 ma) La Garita, CO (25 ma)

## Slide 22: Site of the Toba eruption 74,000 years ago in northern Sumatra
105 km caldera

## Slide 23
Toba eruption, “nuclear winter”

## Slide 24
Current level = 400 ppm
Toba Taupo
Younger Dryas
Dust concentration in ice cores

## Slide 25: Our work – the mysterious Younger Dryas ice age (Greenland Stadial 1 GS-1) Problem: these changes happened so rapidly!
Paris Accords: +1.5 C (2 C?) in 85 years
Dryas: ± 10 C in~150 years (1,2)
Younger Dryas ± 9 C in ~ 22 years (5,7)

## Slide 26: Millimeter wide annual layers in Greenland Ice Cores

## Slide 27: NSF/NOAA Greenland Summit site 38o 28’ 11.4” west, 72o 34’ 25.25” N, elevation 3192 m (10,533 ft)

## Slide 28
DELTA Group slotted 8 DRUM Impactor
8 size ranges:
  Inlet ( ~ 12) to 5.0 μm
  5.0 to 2.5 μm
  2.5 to 1.15 μm
  1.15 to 0.75 μm
  0.75 to 0.56 μm
  0.56 to 0.34 μm
  0.34 to 0.26 μm
  0.26 to 0.09 μm
10.4 l/min, critical orifice control, ¼ hp pump
6.5 x 168 mm Mylar strips
For 42 day run, 4 mm/day,
time resolution = 1 hr.
Field portable
  10 kg, 43 × 22 × 13 cm
43 cm
Optically efficient aerosols

## Slide 29: Example: Stage 8 of DRUM , 0.26 > Dp > 0.09 µm diameter, showing strong diurnal pattern; the deposit shown covers 3 weeks. This is from South Lake Tahoe

## Slide 30
DELTA Group slotted 8 DRUM Impactor
8 size ranges:
  Inlet ( ~ 12) to 5.0 μm
  5.0 to 2.5 μm
  2.5 to 1.15 μm
  1.15 to 0.75 μm
  0.75 to 0.56 μm
  0.56 to 0.34 μm
  0.34 to 0.26 μm
  0.26 to 0.09 μm
10.4 l/min, critical orifice control, ¼ hp pump
6.5 x 168 mm Mylar strips
For 24 week run, 1 mm/day,
time resolution = 12 hr.
Field portable
  10 kg, 43 × 22 × 13 cm
43 cm

## Slide 31
UC Davis DRUM sampler in tunnel under circa 6 feet of snow

## Slide 32: Greenland DRUM strips against white background Date scale is approximate; fine soot from Summit diesels will set final dates
10 to 5.0
5.0 to 2.5
2.5 to1.15
1.15 to 0.75
0.75 to 0.56
0.56 to 0.34
0.34 to 0.26
0.26 to 0.09
July 16 2015 8/1 9/1 10/1 11/1 12/1 1/1 2/1 3/1 4/1 5/1 June 1

## Slide 33: The UC Davis/Lawrence Berkeley NL Advanced Light Source aerosol S-XRF microprobe – 250,000 analyses, mostly for climate studies, continuous DRUM 8 size modes, each with 32 elements, to pg/m3, 1999 – 2007
X-ray beam
DRUM strip

## Slide 34: A “White Beam”? You have got to be kidding!
In x-ray fluorescence analysis, scientist have avoided using broad spectrum “white beams” for years, because
  a. They give a high continuous background, reducing sensitivity,
  b. They make calculations of quantitative yields difficult, and
  c. Self absorption corrections in thick samples are hard
For this reason, modern XRF uses Bragg crystals to get monochromatic x-ray beams whenever possible.
  a. But there is a price to pay – costs 99.9% of flux
But synchrotron x-rays are plane polarized
  a. We moved the detector to 90o - removes 99% background
  b. We wrote programs to make calculations easy and accurate
  c. We have thin samples - no self absorption problems
Net result: world class accuracy and sensitivity for ~ 42 elements in 30 sec

## Slide 35: Synchrotron-X-Ray Fluorescence (S-XRF) spectrum, 30 sec, and AXIL analysis of a remote area aerosol sample. The polarized S-XRF beam suppresses the background by a factor of about 100 versus standard XRF.
Co57 standard for dead time
10,000 cts/channel
1 ct/channel
1 ng/m3
Background without use of the plane polarized x-rays

## Slide 36: Continuous sampling – inlet at surface, but DRUM in tunnel under 3 m of snow
Optically efficient aerosols
December January February March April

## Slide 40: Some Results
The deposition of soils into the Greenland ice cores represents only the small very coarse fraction of the aerosols above the ice sheet
The aerosols that do not deposit are the ones that are most optically active
These aerosols represent a significant increase in the Earth albedo and thus represent a cooling influence
Thus there was much more cooling by dust during the Younger Dryas ice age than previously thought
We propose to study these impacts by direct S-XRF analysis of freeze dried ice cores – resolution? 1 month

## Slide 41: Current threats: - 1,000 years to + 85 years - UCD data on Greenland aerosols
We now have 13 years of data on aerosol at the Greenland Summit site classified by
  8 size modes
  12 hr time increments
  Up to 42 S-XRF elements in each size mode
  Optical absorption
Natural aerosols such as dust, forest fire smoke volcanoes, etc relevant to ice cores
Anthropogenic aerosols from power plants, transport, industry and human initiated fires

## Slide 42: The original northern hemisphere hockey stick graph of Mann, Bradley & Hughes 1999, smoothed curve shown in blue with its uncertainty range in light blue, overlaid with green dots showing the 30-year global average of the PAGES 2k Consortium 2013 reconstruction. The red curve shows measured global mean temperature, according to HadCRUT4 data from 1850 to 2013.

## Slide 43: Carbon dioxide for the past 1,000 years
400 ppm

## Slide 45
Recent understanding: the oceans have a major impact on global temperature – i.e., El Nino warms, La Nina cools the world

## Slide 46
Short wavelength cycle
Long wavelength cycle

## Slide 47: Older Soviet designed power plants burn coal at low temperatures – result, soot. The soot coats dust aerosols and changes them from cooling to heating the world

## Slide 48: Continuous sampling – inlet at surface, but DRUM in tunnel under 2 m of snow
December January February March April

## Slide 49: Continuous sampling – inlet at surface, but DRUM in tunnel under 3 m of snow
USA
China
December January February March April

## Slide 50: Sulfates in Greenland ice cores; US and Europe only? Note poor match > 1980
China

## Slide 51
China
Sahara

## Slide 53: Greenland Summary
The combination of aerosols collected by size, time, and composition, pioneered by our department, when combined with global transport models, allow source identification over much of the Northern Hemisphere
US and European aerosols, dominated by sulfates, tend to cool the Earth
Chinese, Indian, and Indonesian aerosols, rich in soot, tend to heat the Earth
Chinese aerosols arrive at Greenland across the North Pole, doubling the impact of the US and Europe on Greenland
The same process could have operated during the Younger Dryas event

## Slide 54
Good news! Carbon emissions have been almost flat for the past 3 years
Bad news! 2014, 2015, and 2016, each was the hottest year ever.
Bad news! Emissions are still far greater than the Earth can sequester, so CO2 levels continue to rise.

## Slide 55: And the future…..
The hard work of global climate research desperately needs the techniques of modern experimental physics
The hard work of global climate research needs new young scientists who both
  Know the needs of the GCM research
  Know the techniques of physics
Each year in Boulder NOAA hosts a major meeting for Climate Monitoring and Diagnostic Laboratories (CMDL) GCM scientists.
  Heads and key staff of all 5 NOAA CMDL sites, include Antarctica
  NOAA, NCAR, NASA, and DOD GCM modelling teams
  WMO climate and modelling groups from all over the world
  Scientists from CMDL associated university programs
The room holds ~ 120 people

## Slide 56: And the future…..
The hard work of global climate research desperately needs the techniques of modern experimental physics
The hard work of global climate research needs new young scientists who both
  Know the needs of the GCM research
  Know the techniques of physics
What next?
  NSF Greenland upgraded (CNL, SSRL) and continued to 2021.
  NSF high time resolution (monthly?) SXRF analyses of Greenland ice cores for the Younger Dryas event (with UNR Desert Research)
  NSF (1/31/2017) proposal to statistically mix DRUM aerosols, climate gasses, and HYSPLIT trajectories at Mauna Loa Observatory establish the input of Chinese CO2 emissions on the annual CO2 cycle.

## Slide 57
  References:
  Best summary of DELTA Group programs; http://delta.ucdavis.edu
  Best article on Greenland: VanCuren, Richard, Thomas Cahill, John Burkhart, David Barnes, Yongjing Zhao, Kevin Perry, Steven Cliff, and Joe McConnell, Aerosols and their sources at Summit Greenland – First results of continuous size- and time-resolved sampling. Atmospheric Environment, 52:82-97 (2012) doi:10.1016/j.atmosenv.2011.10.047
Best article on DRUM technology: Raabe, Otto G., David A. Braaten, Richard L. Axelbaum, Stephen V. Teague, and Thomas A. Cahill. Calibration Studies of the DRUM Impactor. Journal of Aerosol Science. 19.2:183‑195 (1988).
Best article on our SSRL Beam Line: S.R. Barberie, T.A. Cahill, C.F. Cahill, T.M. Cahill, C.R. Iceman, D.E. Barnes. UC Davis XIPline ("zipline") end-station at the Stanford Synchrotron Radiation Lightsource: Development and experimental results. Nucl. Instrum. Meth. Phys. Res. A: Accelerators, Spectrometers, Detectors and Associated Equipment 729:930-933 (2013) doi:10.1016/j.nima.2013.08.043
Best example of our S-XRF at SSRL: Jenniskens, P, Fries, M. D. Qing-Zhu, Y. ….Cahill, T.A., Barnes, D. E., …Verosub, K. …(55 more)…Radar-enabled recovery of the Sutter’s Mill Meteorite, a carbonaceous chondrite regolith breccia. Science, 338:1583-1587 (2012) doi: 10.1126/science.1227163

## Slide 59: Map of the Earth, ~ 850 to 650 million years ago

## Slide 60: What went wrong? Supercontinent of Rodinia, 1100 my to 650 my, had lots of land mass at the Equator ( ~ same fraction as today!).

## Slide 61: At ~ 850 myears ago, an event triggered a sudden cooling of the Earth
Iceland, April 17, 2010, Eyjafyallajokull Volcano, Volcanic Explosive Index
(VEI) 4
4 | 10 to 25 km | 100 millions m3 | Vulcanian - Plinian | Eyjafyallajokull (2010)
5 | > 25 km | 1 to 10 km3 | Plinian | St. Helens (1980)
6 | > 25 km | 10 to 100 km3 | Plinian – Ultra Plinian | Krakatau (1883) ~ -1.2 C, 3 yrs
7 | > 25 km | 100 to 1000 km3 | Ultra Plinian | Pinatubo (1991), -0.5 C Tambora (1815)
8 | > 25 km | 2,800 km3 2,400 km3 5,000 km3 | Ultra Plinian | Toba (74 ka), Yellowstone, (2.1 ma) La Garita, CO (25 ma)

## Slide 62: One model of a Slushball Earth: Requirements: 1. Significant continental land mass near the equator, and 2. A trigger event cools a) asteroid impact b) super volcano c)other 3. Snow at low latitudes – albedo from 0.28 to 0.60; then oceans start to freeze, from 0.06 to 0.60
Flood basalt events

## Slide 63: One model of a Slushball Earth: Requirements: 1. Significant continental land mass near the equator, and 2. A trigger event a) asteroid impact b) super volcano c)other 3. What brought us out of it? a) CO2 rose to 13% (vs current 0.04%) b) oceans thaw c) eventually the land mass split up
Flood basalt events

## Slide 64
Cambrian Explosion)
Gaskiers and Baykonur glaciations
Ediacaran biota
Single cell, eukaryotes, and colony biota
Andean glaciation
Volcanic CO2 ~ 13%
?
?
“The Boring Billion”
(X 106)
Land vegetation
?
?
?